rustup target add thumbv7em-none-eabihf (to be run only first time)

1. building our code
cargo build --target thumbv7em-none-eabihf

2. flashing (opening openocd)
*open a new terminal
*change directory to /temp i.e. cd /tmp
*finally run following command

openocd -f interface/stlink-v2-1.cfg -f target/stm32f3x.cfg

3. initiate GDB server (change project name accordingly)
(to do in project terminal)
gdb-multiarch -q target/thumbv7em-none-eabihf/debug/led-roulette

4. connecting gdb server to openocd
target remote :3333

5. loading our program to stm
load

Debugging
break main
break = to stop program at break points
continue = to continue execution of program from one break point to next breakpoint

TUI (text user interface)
1. to go to next slide in gdb termina
layout src

2. for disabling tui mode we can run in gdb
tui disable

3. for resetting the program to initial state while debugging run
monitor reser halt

4. for termnating gdb session
quit

Commands
Step: for moving to next line
print: for printing values of variables
info locals: for printing all values of variables at once
clear shell: for clearing tui screen

For using itmdump

1. open openocd same as previously
2. open new terminal, change directory to /tmp . Create new file “touch itm.txt” . Now run “itmdump -F -f itm.txt” .
3. now go to project directory, and build code.
4. open gdb server. (remember to change the project name and avoid number), execute remaining commands.
5. monitor tpiu config internal itm.txt uart off 8000000 (run this command in same gdb terminal)
6. monitor itm port 0 on (this command off all the itm ports and on port 0 only)
7. break main
8. continue
9. next
10.